Doctoral Qualifying Exam
Averaging Schemes for Assessment of Incident and Absorbed Power Density on
Skin Surface
Candidate: Ante Kapetanović
Supervisor: prof. Dragan Poljak, PhD
January 26th, 2023

---
Table of Contents
1. General Introduction in Human Exposure to EMFs
2. Exposure Assessment and Dosimetry in Era of 5G
3. State of Research
  1. Tissue Models and Control Surfaces
  2. Power Density Averaging Schemes
4. Conclusion and Future Work
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
1. General Introduction in
Human Exposure to EMFs
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
EM Radiation
- is created due to periodic changes of
  electric and/or magnetic fields
- Periodicity → frequency
- Non-ionizing vs. ionizing radiation
  - Single photon energy up to vs. above 10 eV
- EM waves in lossy medium transfer kinetic energy
  to surrounding bounded atoms/molecules of material → “vibrations” → temperature rise
  - Wavelength of the incident field ~ dominant dimension of material
  - Biological tissue ~ microwave up to low-energy UV spectrum
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Non-Ionizing EM Radiation Effects
on Biological Tissue
- are any change (physical, chemical, or mechanical) induced in tissue
- Feedback repair mechanism
  - Preservation of homeostasis within threshold limits
- Limits exceeded → adverse health effects
- Non-thermal vs. thermal effects
  - Frequency dependent with transition at ~100 kHZ
- Non-thermal effects at RF → no scientific consensus
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Summary of Non-Ionizing Radiation Effects
on Biological Tissue
exposure to	static / H-fields	LF	RF	IR	visible / light	low-energy / UV
frequency / [Hz]	0	1 / up to / 100 k	100 k / up to / 300 G	300 G / up to / ~400 T	~400 T / up to / 790 T	> 790 T
interaction effects	induced fields & currents	stimulation of excitable cells	→←	tissue heating
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Assessment Basis for Heating Effects
- Interaction between induced E-fields and polar molecules within tissue → kinetic energy
- Increased kinetic energy → frequent interaction of polar molecules and charged particles → thermal energy
- Heating effects depend on the distribution of EM power within exposed tissue
  - Steady state conditions vs. brief exposure
  - Local vs. whole-body exposure
  - Tissue type-1 vs. type-2
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Power transmission and penetration depth
into dry skin
Homogeneous block of tissue with dielectric properties of dry skin.
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Limiting Exposure to Artificial EMFs
- Widespread use of wireless RF consumer electronics
- International bodies prescribe exposure limits within guidelines (ICNIRP) or standard (IEEE C95.1)
  - Occupational vs. general public
- Protection against adverse health effects – respecting the frequency and exposure scenario dependent limits
  - Derived upon published literature
  - Applied reduction factors
- Threshold values → BRs → RLs
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
(Very) Brief Historical Overview
- 1960s – Tri-service program, first set of C95.1.x
- 1970s – large number of wireless devices operate in close proximity of human body → public distrust → many controversies
- 1970/80s – termographic studies, comprehensive environmental studies → RF dosimetry handbook1
- 1990s – IRPA → INIRC → ICNRIP
- 2020s – new C95.1 standard2 and ICNIRP guidelines3
1 Durney et al. Brooks Air Force Base, TX: USAF School of Aerospace Medicine, AFSC, 1986
2 IEEE Std C95.1-2019:1–312, 2019
3 ICNIRP, Health Physics 118:483–524, 2020
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Evolution of research related to
bioeffects of RF fields
(50s to date)
Compiled from the database of publications at http://emf-portal.org.
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
2021 studies related to
bioeffects of RF fields
Compiled from the database of publications at http://emf-portal.org.
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Dosimetric Quantities in Terms of BRs
- are derived from the levels of RF EMFs that correspond to (operational) adverse health effects
- are frequency dependent dosimetric quantities at the appropriate spatio-temporal scale of exposure, e.g.:
  - Whole-body exposure (over 30 min): SAR = 4 W/kg ~ 1 °C
    - Reduction factors of 10 for workers and 50 for general public
  - Local exposure up to 6 GHz (over 6 min): 10-g or 1-g SAR
  - Local exposure above 6 GHz (over 6 min): 4-cm2 or 1-cm2 APD
    - Reduction factor of 2 for workers and 10 for general public
- RLs provide more practical means of demonstrating compliance by estimating IPD in free space
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
2. Exposure Assessment and Dosimetry in
Era of 5G
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
~ 90% EM power is dissipated in
the uppermost skin layer
above 6 GHz
Homogeneous block of tissue with dielectric properties of skin
exposed to a plane wave of 100 mW/cm2.
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Definition of the Spatially Averaged APD
Derived from the Poynting vector
- A – frequency-dependent averaging area
- E, H* – peak values of the electric and complex-conjugate magnetic fields
- n – unit normal vector on A
- dA – integral element of A
S _ "ab, 1" = 1 over {2 A} iint from {A} {Re left [ bold {E} × {bold {H}} ^ {∗} right ] {} bold {n} {} dA}
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Definition of the Spatially Averaged APD
via Volume-Averaged SAR
- Tissue surface is positioned at z = 0
- zmax should be sufficiently larger than the EM penetration depth
- ρ – tissue density in kg/m3
- SAR is defined as
- σ – tissue conductivity in S/m
S _ "ab, 2" = 1 over {2 A} iint from {A} dA int from {z = 0} to {z_max} %rho { } "SAR" { } dz
%sigma { } lline bold {E}^2 rline / %rho
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Practical Considerations for
Power Density Spatial Averaging
- [2, 6] GHz → peak value of the incident PD
- > 6 GHz → averaging across 4 cm2 square
  evaluation plane4, 5
- > 30 GHz → averaging across 1 cm2 area in addition to 4 cm2 to account for narrow beams
  at high frequencies6
4 Hashimoto et al. Phys. Med. Biol. 62(8):3124–3138, 2017
5 Funahashi et al. IEICE Trans Electronics 8:644-646, 2018
6 Foster et al. Health Physics 111(6):528-541
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Sab, 1 and Sab, 2 are equivalent
provided that the surface surrounding a given volume of the tissue is closed and no active sources are present in this volume of interest
Mathematical details are omitted for your – you are welcome ,
but can be found in
Doctoral Qualification Paper in
Chapter 3.3.2.
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Mathematical Defintion of the IPD
- Modulus of the time-averaged power density vector
- Assuming that the separation distance is
  ⪎ λ/2π,
  spatially averaged IPD is
  a valid proxy for
  local max. temp. rise7
S _ "inc" = lline bold {E} × {bold {H}} ^ {∗} rline
S _ "inc, n" = 1 over {2 A} iint from {A} {Re left [ bold {E} × {bold {H}} ^ {∗} right ] {} bold {n} {} dA}
S _ "inc, tot" = 1 over {2 A} iint from {A} { left lline Re left [ bold {E} × {bold {H}} ^ {∗} right ] right rline {} dA}
7 IEEE Std 2889-2021:1–152, 2021
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
3. State of Research
3.1. Tissue Models and Control Surface
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Tissue-Equivalent Model Configuration
- 1- or 3-/4-layer block tissue model8 > 6 GHz
- Anatomy of skin
horny layer	clear layer	granular layer	prickle cell layer	basal cell layer	papillary layer	reticular layer
epidermis					dermis
- Hypodermis – low heat transfer → thermal barrier
- Muscle
- Dielectric properties ← 5-term Cole-Cole model9
8 Ziskin et al. Bioelectromagnetics 39(3):173-189, 2018
9 Gabriel. TR-1996–0037, US Air Force, 1996
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Control Surface during Spatial Averaging on
the Multi-Layer Tissue-Equivalent Block Model
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
3. State of Research
3.2. Power Density Averaging Schemes
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Prior to IEEE C95.1 and ICNIRP 2020...
- ICNIRP 199810
  - Whole-body exposure above 10 GHz in the far-field zone → the IPD spatially averaged on 20 cm2 planar control surface
  - Local exposure → the spatially-averaged IPD over the most exposed region of 1 cm2
- IEEE C95.1-199911
  - Spatial averaging – the root-mean-square of the power density over an area equivalent to the vertical cross-section of the human body (projected) at a distance of no less than 20 cm
10 ICNIRP, Health Physics 74 (4):494-522, 1998
11 IEEE Std C95.1-1999:1–83, 1999
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
State of the Art
- Transition frequency of 6 GHz
  - Anderson et al 201012, McIntosh and Anderson 201013
- Harmonization of control surfaces between standards
  - Colombi et al 201514, Thors et al 201615, Xu et al 201816
- Square averaging surface of 2 x 2 and 1 x 1 cm2
  - Hashimoto et al 20174
- Spatially averaged transmitted power density
  - Funahashi et al 201817
12 Anderson et al. Bioelectromagnetics 31(6):454–466, 2010
13 McIntosh and Anderson, Bioelectromagnetics 31(6):467–478, 2010
14 Colombi et al. IEEE Antennas Wirel. Propag. Lett. 14:1247–1249, 2015
15 Thors et al. IEEE Access 4:7469–7478, 2016
16 Xu et al. IEEE Access 6:830–838, 2018
17 Funahashi et al. IEEE Access 6:77665-77674, 2018
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Going beyond the State of the Art
- Non-planar body parts, e.g., fingers18, ears19, with the curvature radius ~ wavelength of the incident EMF
  → underestimation of the area-averaged qauntities
- Non-planar tissue models currently discussed within IEEE ICES TC95 SC6 WG7
  - Canonical shapes, e.g., sphere & cylinder
  - Anatomical models
18 Li et al. IEEE Trans. Microw. Theory Tech. 60(7):2267–2276, 2012
19 Sacco et al. IEEE J. Electromagn. RF Microw. Med. 6(3):413–419, 2022
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Spherical Model with Radius Set to 5 cm20, 21
20 Kapetanovic and Poljak. IEEE Trans. Electromagn. Compat. 64(5): 1296–1303, 2022
21 Kapetanovic et al. In proceedings SoftCOM 2023
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Cylindrical Model With Radius Set to 5 cm22
22 Kapetanovic and Poljak. To appear in Radiat. Prot. Dosimetry, 2023
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Reference Averaging Surface for
Non-planar models23
(a) and (b) L1 - parallel to the grid axis to match the standard evaluation plane
(a) and (b) L1 - bent along the surface to match the curvature of skin
Side bounds - parallel to the grid axis in (a) and (c)
Side bounds - parallel to the internal E-field gradients at the surface in (b) and (d)
L4 - defined as the contour where the E-field is at 1/1000 of max value in the volume
23 Diao and Hirata. 55(22):224001, 2020
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
4. Conclusion and Future Work
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Summary
- Recent updates of international exposure limits are motivated with the deployment of 5G worldwide
- Steady-state local exposure above 6 GHz – APD/IPD
- Valid proxies for temperature rise on flat surfaces
- Curvature of local body parts is pronounced → compromised accuracy & compliance assessment
- Future work
  - Analytical spatial averaging on non-planar surfaces (ICES TC96 SC6 WG7)
  - Numerical & data-driven techniques for surface integration across conformal surfaces of anatomical tissue models
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Thank You for Your Attention
Q&A
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface

---
Abbreviations in Order of Appearance
- EMF – electromagnetic field
- 5G – fifth generation
- EM – electromagnetic
- UV – ultraviolet (radiation)
- RF – radio-frequency
- LF – low-frequency
- IR – infrared (radiation)
- ICNIRP – Internation commission on non-ionizing radiation protection
- IEEE – Institute of Electrical and Electronics Engineers
- BR/DRL – basic restriction or dosimetric reference limit
- RL/ERL – refernce level or exposure reference level
- IRPA - International Radiation Protection Association
- INRC – International Non-Ionizing Radiation Committee
- SAR – specific absorption rate
- APD – absorbed power density
- IPD – incident power density
Doctoral Qualifying Exam	Averaging schemes for Assessment of Incident and Absorbed Power Density on Skin Surface